## Slide 1: NAT & IPTables
From ACCEPT to MASQUERADE
Tim(othy) Clark (eclipse)

## Slide 2: NAT
IPv4 Hack
One external IP for a whole network
Used commonly in home routers
All external traffic goes through the router
Notes: Ok so what is a NAT, it is essentially a hack to try and overcome the lack of ipv4 addresses [Bullet], it essentially gives an entire internal network a single external ip address [bullet], it is commonly used with home networks [bullet], so your router has an external ip assigned by your isp and it has an internal ip assigned by itself (commonly 192.168.0.1), so all traffic going through the router to the outside appears to come from the routers external ip, and then the router sorts out the responses and sends them to the right place.[end slide]

## Slide 3: IPTABLES
Packet Filtering
Packet Manipulation
Creates firewalls
NATs
Cool stuff
Notes: IPTABLES is the network packet filtering [bullet] and manipulation [bullet] tool for linux, it lets users create firewalls[bullet] and create NATs[bullet] and allows lots of other cool stuff[bullet] such as transparent proxying.[end slide]

## Slide 4: Command Structure
IPTABLES –A INPUT –s 137.44.10.0/24 –j DROP
“-A chain” adds rules to a chain
This is followed by a match
And then an action
Can match on lost of things
Can ACCEPT, DROP or jump to a user defined chain
Notes: This is an example of an iptables command[eg]The default table is filter so is not necessary to declare it. –A adds rules to the specified chain[bullet], -D removes them, this is followed by a matching condition[bullet] and a jump or action[bullet]. Packets can be matched on lots of different things and in combination[bullet], -s shown, matches by IP or IP range. Common actions are ACCEPT, DROP or a user chain name[bullet], if it is a chain name then this chain is traversed. The example will drop all packets coming from SUCS.[end slide]

## Slide 5: Tables, Chains and Rules
Tables define basic usage
Chains contain rules that are checked till one is executed
Different built in chains execute in different paces
Rules execute actions on packets that match the condition.
Notes: Iptables works with tables that contain chains which contain rules. Tables define basic usage and where it is applied, there are filter, nat, mangle and raw table[bullet], im going to talk mostly about the filter table and a brief bit in the nat table. Tables contain chains, they all have some built in chains and you can add custom chains, a chain is a collection of rules that are checked until one is executed[bullet], built in chains are executed on packets in different places such as the input chain in the filter table is execute on packets going into the software of the system[bullet]. Built in chains have a policy, which is executed if no rules are matched. Rules define a condition and an action to do if the condition is matched.[end slide]

## Slide 6: Example Traversal
Incoming Packet
–A INPUT –s 137.44.10.0/24 –j DROP
–A INPUT –s 137.44.0.0/16 –j ACCEPT
–P INPUT DROP
Source: 137.44.10.6
Matching
DROP

## Slide 7: Example Traversal
Incoming Packet
–A INPUT –s 137.44.10.0/24 –j DROP
–A INPUT –s 137.44.0.0/16 –j ACCEPT
–P INPUT DROP
Source: 137.44.195.83
Matching
Not Matched
Matching
ACCEPT

## Slide 8: Example Traversal
Incoming Packet
–A INPUT –s 137.44.10.0/24 –j DROP
–A INPUT –s 137.44.0.0/16 –j ACCEPT
–P INPUT DROP
Source: 64.233.183.104
Matching
Not Matched
Matching
Not Matched
Policy
DROP

## Slide 9: Connection Tracking
Detects replies to sent packets
Matching module
NEW is starting a new connection
ESTABLISHED is for existing connections
RELATED is for new connections related to existing ones
Notes: Connection tracking is used to track what data is sent and to recognise the replies to data that was sent[bullet], packets can be matched on their status[bullet], they get clisified into 3 catogories, NEW, RELATED and ESTABLISHED. New shows it is a new connection[bullet], ESTABLISHED shows it is part of an already established connection[bullet], and RELATED is staring a new connection but it is related to an existing connection.[bullet] This allows packets to be accepted only in response to outgoing connections creating a firewall.[end slide]

## Slide 10: Masquerade
Used in the prerouting chain of the nat table
Makes NAT work
Changes destination and source addressed as appropriate
Notes: Masquerade uses similar technology to connection tracking to modify data being forwarded, it is used in the prerouting chain of the nat table[bullet], this is what does the NAT[bullet], it changes the destination and source addresses of packets being forwaded as appropriate to make the nat work [bullet].
[end slide]

## Slide 11: Example Masq Code
Internal interface is eth1
External interface is eth0
Example configuration:
iptables –P INPUT DROP
iptables -P FORWARD DROP
iptables -A FORWARD -m state --state RELATED,ESTABLISHED -j ACCEPT
iptables –A FORWARD -i eth1 -j ACCEPT
iptables –t nat -A POSTROUTING -o eth0 -j MASQUERADE
echo 1 > /proc/sys/net/ipv4/ip_forward
Notes: Internal interface = eth1
External interface = eth0
(1): Set the policy for the input chain
(2): Set the policy for the forward chain
(3): Allows existing connections to be forwarded
(4): Allows all data from the internal network to be forwarded
(5): Enables masquerading for data going to the output interface
(6): Enables ipv4 packed forwarding

## Slide 12: Useful Bits
iptables-save stores the configuration in a file
iptables-restore restores the configuration from a file
Easily write scripts to restore it
iptables has a good manual page
Notes: The configuration example on the previous slide disappears when you reboot, but you can store it with commands[bullet]. And this can be configured to auto configure itself when linux boots[bullet]. Also iptables has a really good man page[bullet] so if you want to know what you can use to match packets or what else it can do the first place you can look[end of slide]

## Slide 13: Any Questions?
Notes: (Sorry for the time its taken and )[bullet] any questions?